## Slide 1
James Clark and James Sherwood
Green Chemistry Centre of Excellence, University of York, UK
The world’s leading Centre for Green and Sustainable
research, training and commercialisation
Green Chemistry and HSP
Towards an intelligent approach to solvent substitution
Green Chemistry @ York

## Slide 2
Biorenewables Development Centre
Green Chemistry Centre
Ideas
Commercial Products
Laboratory & Desk-top Studies
Training for industry partners
Proving routes & technologies
Scale-up & Application Studies
Environmental Impact Assessments
Speculative
Research
Discovery
Focussed Research
Industrial Collaboration
Applied Research
Green Chemistry at York: from research bench to semi-scale
Green Chemistry has to work!!!
Notes: 2

## Slide 3
Renewable Resources and Materials
Microwave Chemistry and Processing
Natural and Bio-derived Solvents
Clean Synthesis and Platform Molecules
From waste to wealth using Green Chemistry
Our Technology Platforms
And… Carbon Dioxide Chemistry

## Slide 4
Benefits of the Chemical Industry
But its not sustainable…..in products, process or resources….
97% of all goods are manufactured
using at least one chemical reaction
Notes: 4
4

## Slide 5
REACh!
We are using non-renewable, diminishing resources.
Making more waste than product, and using dangerous substances

## Slide 6
We are heavily reliant on non-renewables......but our crude oil reserves are finite
> 90% of chemicals are manufactured from oil and gas
BUT time is running out for petrochemical feedstocks…and for other resources...

## Slide 7
Fuels
Solvent
Bulk chemicals
Plastics
Fibres
Fine chemicals
Oils
Bio-refinery
Biomass
Don’t use food quality feedstocks!!

## Slide 8
Johan Sanders - Wageningen University, The Netherlands Biorefinery,
the bridge between Agriculture and Chemistry
75 billion € 60€/ T of biomass 1200 Mt CO2 savings
97 billion € 80€/ T of biomass 1200 Mt CO2 savings
180 billion € 140€/ T of biomass 1500 Mt CO2 savings
Biorefining will improve the process economics
(Energy -> Fuels -> Chemicals)
125 M hectare = 0.8% world land area

## Slide 9
Cosmetics
Plastics industry
Metal cleaning
Agrochemicals
Food sector
Dry cleaning
Other industries
Home cleaning
Adhesives
Inks
Paints/coatings
Pharma
Solvent is needed in manufacturing & processing
Solvent used for washing
Market: 20 Million
Tonnes /year
ESIG data, 1997
Solvent Market

## Slide 10
1 kg of API necessitates more than 100 kg of material
  Cleaning is not included!
Solvents and water represent ca 75% of these
  Reduce the impact by reduction of solvent & water amount
  Use the “greenest” solvents
In Pharmaceutical Manufacturing
Chem21 was set up to tackle such issues….
Chem21.eu

## Slide 11
CHEM21 SOLVENT GUIDE
But existing solvents are not enough…
we need new, preferably bio-based solvents

## Slide 12
echa.europa.eu/regulations/reach/authorisation/the-candidate-list
echa.europa.eu/candidate-list-table
REACH is making it worse….
Regulation (EC 1907/2006)
Substances of Very High Concern (SVHC)
An opportunity for bio-based solvents?
Notes: The first step in the authorisation process is to identify those substances that may have serious effects on human health or the environment and, therefore, the risks resulting from their use must be properly controlled and the substances progressively replaced when possible.
A Member State or ECHA at the request of the European Commission, can propose a substance to be identified as a Substance of Very High Concern (SVHC). If identified, the substance is added to the Candidate List, which includes candidate substances for possible inclusion in the Authorisation List (Annex XIV).

## Slide 13
Green chemistry and solvents
Solvent replacement
Green Chemistry Principle #5
The use of auxiliary substances (e.g., solvents, separation agents, etc.) should be made unnecessary wherever possible and, innocuous when used.
https://www.acs.org/content/acs/en/greenchemistry/what-is-green-chemistry/principles/12-principles-of-green-chemistry.html

## Slide 14
Green chemistry and solvents
The hazards
http://www.japantimes.co.jp/news/2013/04/02/national/printing-firm-raided-over-workers-bile-duct-cancer/#.WMfC2X9nDRY; http://www.bbc.co.uk/news/uk-scotland-tayside-central-35151700.

## Slide 15
Bio-based solvents. Renewable, but equally toxic.
J. H. Clark et al., Int. J. Mol. Sci., 2015, 16, 17101.
Green chemistry and solvents
The solution?

## Slide 16
Levoglucosenone
Opportunities for different solvents
Selective pyrolysis of biomass (e.g. sawdust) produces a new bio-based platform molecule.
G. R. Court et al., US Pat. 2012/0111714, 2012.

## Slide 17
Levoglucosenone
Derivitisation
X=Y=H (hydrogenation)
X=OMe, Y=H (Michael addition)
X=OH, Y=(CH2)n (ketalisation)
X=OMe, Y=H (alcoholysis)
Cycloaddition also possible

## Slide 18
Levoglucosenone
An intermediate for bio-based solvents
Dihydrolevoglucosenone (Cyrene™) is easily made by the hydrogenation of levoglucosenone.
J. Sherwood et al., Chem. Comm., 2014, 50, 9650.

## Slide 19
Cyrene™
Proof of concept using HSP
Cyrene
P
H
NMP
HSPiP, 5th edition, version 5.0.03, 2015.

## Slide 20
Cyrene™
Applications in synthesis
J. Sherwood et al., Chem. Comm., 2014, 50, 9650.

## Slide 21
Cyrene™
Applications in materials

## Slide 22
Cyrene™
Graphene dispersion: solvent selection
H.J. Salavagione et al., Green Chem., 2017, advanced article. DOI: 10.1039/C7GC00112F .

## Slide 23
Cyrene™
Graphene dispersion: solvent selection
Phase 1: properties
HSPiP, 5th edition, version 5.0.03, 2015.

## Slide 24
Cyrene™
Graphene dispersion: solvent selection
Priority bio-based solvents (51) …
… with the correct polarity (18) …
… and the right surface tension (6) …
… and a suitable viscosity (5) …

## Slide 25
Cyrene™
Graphene dispersion: solvent selection
EU regulation (EC) No 1907/2006 for the Registration, Evaluation, Authorisation & restriction of CHemicals (REACH); European regulation (EC) 1272/2008 on classification, labelling and packaging of substances and mixtures (CLP).
Phase 2: regulatory status
Level 1= REACH for restriction
  Carcinogenic or mutagenic or reprotoxic (CMR)
  Persistant and bio-accumulating and (eco)toxic (PBT)
Level 2 = GHS CLP for labelling
  Acute toxicity
  Environmental hazard

## Slide 26
Cyrene™
Graphene dispersion: solvent selection
Bio-based solvents with the required performance characteristics:
Butyl lactate
Cyrene™
Furfural
Tetrahydrofurfuryl alcohol
Triacetin
These petrochemical solvents also pass:
1,2-Dichlorobenzene
Benzonitrile
Cyclohexanone
Cyclopentanone
Pyridine

## Slide 27
Cyrene™
Graphene dispersion: solvent selection
Phase 3: green metrics
1,2-Dichlorobenzene
Benzonitrile
Butyl lactate
Cyclohexanone
Cyclopentanone
Cyrene™
Pyridine
Triacetin
NMP

## Slide 28
Cyrene™
Graphene dispersion: results
H.J. Salavagione et al., Green Chem., 2017, advanced article. DOI: 10.1039/C7GC00112F .

## Slide 29
Cyrene™
Graphene dispersion: results
A holey carbon grid coated with a number of graphene flakes.
A single graphene flake.
The border area of the flake in (b), magnified.
A larger single graphene flake and a smaller flake underneath.
TEM analysis of Cyrene dispersed graphene.

## Slide 30
Cyrene™
Graphene dispersion: results
Dots: Graphene concentration in Cyrene™ (mg/mL)
Bars: AD/AG (Raman spectroscopic analysis)
As a function of time /minutes
15 30 45 60 120
NMP
Cyrene™
Triacetin

## Slide 31
Cygnet
Another levoglucosenone solvent
A. Alves Costa Pacheco et al., ChemSusChem, 2016, 9, 3503.
‘Easy’ derivatives of Cyrene™ offer different solvent opportunities

## Slide 32
Cygnet
Screening levoglucosenone derivatives
Screening the literature:
Derivatives of levoglucosenone published 1995-2015.
Melting point <100 °C.
Add derivatives: saturated olefins, esters and ethers.
HSP target = DCM
  Level 1: Ra = 3.0 MPa½
  Level 2: Ra = 1.2 MPa½
HSP target = NMP
  Level 1: Ra = 3.0 MPa½
  Level 2: Ra = 2.4 MPa½
96
164
53
15
21
15

## Slide 33
Cygnet
Screening levoglucosenone derivatives

## Slide 34
Cygnet
Matching targets with HSP

## Slide 35
Cygnet
Applications in synthesis
Log(initial rate)
Low boiling solvents
Hydrocarbons
Water
Oxygentated solvents
N/S dipolar aprotics

## Slide 36
York, the University of York and the Green Chemistry Centre of Excellence

## Slide 37: The global picture: the bio-economy is priority worldwide

## Slide 38
G2C2 MEMBERS
2013: 8 Centres 2014: 21 Centres 2015: 31 Centres 2016: 33 Centres

## Slide 39
RenewChem
Promoting sustainable chemical manufacturing
through the use of bio-resources and green chemistry
Industry Club
and
Centre for Graduate Training
The latest GCCE initiative…....

## Slide 40
Research
Industry
Networking
Education
www.greenchemistry.net